Akiko Specification

Akiko Specification

Akiko functions as the main control gate array for the Amiga CD32 Game System (CDGS). It acts as an interface between the processor and the custom chips buffering the data and generating the control signals. It also contains an interface for talking to a CD drive mechanism and a corner turn memory for accelerating Chunky to Planar pixel conversion. This device occupies position U5 in the CD game system.

Configuration

This device is configured as a 160-pin plastic quad flat pack (PQFP) package, with external dimensions as shown in Figure 4-2.

# Pinout

| I « | Input |  |  |
| --- | --- | --- | --- |
| 0 = | Output |  |  |
| B = | Bidirectional |  |  |
| P = | Power |  |  |
| PIN« | NAME | TYPE | Description |
| 1 | VDDE1 | P | Power |
| 2 | PD16 | B | Processor Data |
| 3 | PD17 | B | Processor Data |
| 4 | PD18 | B | Processor Data |
| 5 | PD19 | B | Processor Data |
| 6 | PD20 | B | Processor Data |
| 7 | PD21 | B | Processor Data |
| 8 | PD22 | B | Processor Data |
| 9 | PD23 | B | Processor Data |
| 10 | VSSE4 | P | Power |
| 11 | PD24 | B | Processor Data - |
| 12 | PD25 | B | Processor Data |
| 13 | PD26 | B | Processor Data |
| 14 | PD27 | B | Processor Data |
| 15 | PD28 | B | Processor Data |
| 16 | PD29 | B | Processor Data |
| 17 | PD30 | B | Processor Data |
| 18 | PD31 | B | Processor Data |
| 19 | VDDE3 | P | Power |
| 20 | CDO | B | Custom Chip Data |
| 21 | CD16 | B | Custom Chip Data |
| 22 | CD1 | B | Custom Chip Data |
| 23 | CD17 | B | Custom Chip Data |
| 24 | CD2 | B | Custom Chip Data |
| 25 | CD18 | B | Custom Chip Data |
| 26 | CD3 | B | Custom Chip Data |
| 27 | CD19 | B | Custom Chip Data |
| 28 | CD4 | B | Custom Chip Data |
| 29 | CD20 | B | Custom Chip Data |
| 30 | VSSE5 | P | Power |
| 31 | CDS | B | Custom Chip Data |
| 32 | CD21 | B | Custom Chip Data |
| 33 | CD6 | B | Custom Chip Data |
| 34 | CD22 | B | Custom Chip Data |
| 35 | CD7 | B | Custom Chip Data |
| 36 | CD23 | B | Custom Chip Data |
| 37 | CDS | B | Custom Chip Data |
| 38 | CD24 | B | Custom Chip Data |
| 39 | CD9 | B | Custom Chip Data |
| 40 | CD25 | B | Custom Chip Data |
| 41 | VSS11 | P | Power |
| 42 | CD10 | B | Custom Chip Data |
| 43 | CD26 | B | Custom Chip Data |
| 44 | VSSE1 | P | Power |
| 45 | CD11 | B | Custom Chip Data |
| 46 | CD27 | B | Custom Chip Data |
| 47 | CD12 | B | Custom Chip Data |
| 48 | CD28 | B | Custom Chip Data |
| 49 | CD13 | B | Custom Chip Data |
| 50 | CD29 | B | Custom Chip Data |
| 51 | CD14 | B | Custom Chip Data |
| 52 | CD30 | B | Custom Chip Data |
| 53 | CD15 | B | Custom Chip Data |
| 54 | CD31 | B | Custom Chip Data |
| 55 | VDD13 | P | Power |
| 56 | RAS | I | Processor Reset |
| 57 | AWE | I | Alice Write Enable |
| 58 | SCANEN | I | Test Mode Enable |
| 59 | BCLK | I | CD Bit Clock |
| 60 | VSSE3 | P | Power |
| 61 | CPUCLK | I | CPU Clock |
| 62 | VSSSS3 | P | Power |
| 63 | BCAS0 | 0 | Buffered Cas Byte 0 |
| 64 | BCAS1 | 0 | Buffered Cas Byte 1 |
| 65 | CAS | I | Buffered Cas Byte from Alice |
| 66 | BCAS2 | 0 | Buffered Cas Byte 2 |
| 67 | BCAS3 | 0 | Buffered Cas Byte 3 |
| 68 | ADRAO | I | DRAM Address 0 from Alice |
| 69 | ADRA1 | I | DRAM Address 1 from Alice |
| 70 | RDRAO | I | DRAM Address 0 to DRAM |
| 71 | RAMEN | 0 | RAM Enable/Chip Memory Access |
| 72 | REGEN | 0 | Register Enable/Chip Register Access |

| PIN # (con't) | NAME (cont) | TYPE (cont) | Signal Description (con't) |
| --- | --- | --- | --- |
| 73 | ROMEN | 0 | ROM Enable |
| 74 | DBR | 1 | Chip Data Bus Request |
| 75 | RWE.. | 0 | DRAM Write Enable |
| 76 | IFCLK | 1 | CD Command Interface Clock |
| 77 | IFDAT | B | CD Command Interface Data |
| 78 | IFD1R | 1 | CD Command Interface Direction |
| 79 | LRCLK | 1 | CD Data Loft/Right Clock |
| 80 | VDD12 | P | Power |
| 81 | VDDE2 | P | Power |
| 82 | DATA | 1 | CD-Data Data |
| 83 | C2PO | 1 | CD-Data Errors |
| 84 | 1NT2 | 0 | Interrupt Request (Chips) |
| 85 | INT3 | I | Interrupt Request (Chips) |
| 86 | INT6 | 0 | Interrupt Request (Chips) |
| 87 | BLS | 0 | Blitter Slow Down |
| 88 | SCOR | 1 | CD-Subcode Sync |
| 89 | SUBCL | 0 | CD-Subcode Clock |
| 90 | SUBDAT | 1 | CD-Subcode Data |
| 91 | WFCLK | 1 | CD-Subcode Frame Clock |
| 92 | LED | B | Power On LED / Audio Filter Disable |
| 93 | MUTE | B | Audio Mute Signal |
| 94 | VSSE8 | P | Power |
| 95 | FIREO | B | F«re Button |
| 96 | FIRE1 | B | Fire Button |
| 97 | KBCLK | B | Keyboard Clock (Keyboard) |
| 98 | KBDATA | B | Keyboard Data (Keyboard) |
| 99 | IOPO | B | General Purpose I/O Pin 0 |
| 100 | IOP1 | B | General Purpose I/O Pin 1 |
| 101 | BR | 0 | Bus Request |
| 102 | BG | 1 | Bus Grant |
| 103 | VDDE5 | P | Power |
| 104 | BERR | 0 | Bus Errors |
| 105 | AS | B | Address Strobe |
| 106 | DS | B | Data Strobe |
| 107 | RW | B | Processor Read/Write |
| 108 | SZO | B | Data Transfer Size |
| 109 | SZ1 | B | Data Transfer Size |
| 110 | DSACKO | B | Data Transfer Termination |
| 111 | DSACK1 | B | Data Transfer Termination |

| PIN # (cont) | NAME (cont) | TYPE (cont) | Signal Description (con't) |
| --- | --- | --- | --- |
| 112 | VSSE2 | P | Power |
| 113 | A23 | B | Processor Address Bus |
| 114 | A22 | B | Processor Address Bus |
| 115 | A21 | B | Processor Address Bus |
| 116 | A20 | B | Processor Address Bus |
| 117 | A19 | B | Processor Address Bus |
| 118 | A18 | B | Processor Address Bus |
| 119 | A17 | B | Processor Address Bus |
| 120 | A16 | B | Processor Address Bus |
| 121 | VSS12 | P | Power |
| 122 | EXTACC | 1 | Processor Address Bus |
| 123 | A15 | B | Processor Address Bus |
| 124 | A14 | B | Processor Address Bus |
| 125 | A13 | B | Processor Address Bus |
| 126 | A12 | B | Processor Address Bus |
| 127 | A11 | B | Processor Address Bus |
| 128 | A10 | B | Processor Address Bus |
| 129 | A9 | B | Processor Address Bus |
| 130 | AS | B | Processor Address Bus |
| 131 | VSSE7 | P | Power |
| 132 | A7 | B | Processor Address Bus |
| 133 | A6 | B | Processor Address Bus |
| 134 | A5 | B | Processor Address Bus |
| 135 | A4 | B | Processor Address Bus |
| 136 | A3 | B | Processor Address Bus |
| 137 | A2 | B | Processor Address Bus |
| 138 | A1 | B | Processor Address Bus |
| 139 | A0 | B | Processor Address Bus |
| 140 | VDDE4 | P | Power |
| 141 | PDO | B | Processor Data |
| 142 | PD1 | B | Processor Data |
| 143 | PD2 | B | Processor Data |
| 144 | PD3 | B | Processor Data |
| 145 | PD4 | B | Processor Data |
| 146 | PD5 | B | Processor Data |
| 147 | PD6 | B | Processor Data |
| 148 | PD7 | B | Processor Data |
| 149 | VSSE6 | P | Power |
| 150 | PD8 | B | Processor Data |

| PIN « (con't) | NAME (con't) | TYPE (cont) | Signal Description (con't) |
| --- | --- | --- | --- |
| 151 | PD9 | B | Processor Data |
| 152 | PD10 | B | Processor Data |
| 153 | PD11 | B | Processor Data |
| 154 | PD12 | B | Processor Data |
| 155 | PD13 | B | Processor Data |
| 156 | PD14 | B | Processor Data |
| 157 | PD15 | B | Processor Data |
| 158 | cpll | 1 | CPU Space Cycle (F.P.U) |
| 159 | RESET | B | General Reset |
| 160 | VDD12 | P | Power |